## Slide 1: Networking Lab Project Report
A Comprehensive Analysis of Enterprise Network Architectures
Experiment 6: Smart Office Network Challenge
Experiment 7: Bank ATM Network Simulation

## Slide 2: Project Overview
Demonstration of critical Layer 2 and Layer 3 networking protocols.
1. Experiment 6: Smart Office Network
- VLAN segmentation, ROAS, NAT, and Zero-Trust ACLs.
2. Experiment 7: Bank ATM Network
- Highly available WAN, redundant topology, and OSPF dynamic routing.

## Slide 3: Exp 6: Smart Office Scenario
Aim: Design and secure a multi-department corporate network.
Requirements:
• Departments: HR, Accounts, Developers, Testing, Server Room.
• Access Policy: Only Developers can access the Server Room.
• Privacy: HR data isolated, restricted to outbound internet only.
• Global Connectivity: Outbound internet access via NAT.

## Slide 4: Exp 6: Network Architecture
• VLANs (Virtual LANs): Logical broadcast containment.
• 802.1Q Trunking & ROAS: Efficient inter-VLAN routing.
• NAT Overload (PAT): Maps internal private subnets to public IP.
• Extended ACLs: Strict filtering based on Source/Dest IP & Protocol.

## Slide 5: Exp 6: Testing & Results
• Internet Connectivity: Successful pings to Google Server (8.8.8.8).
• Security Validation: Unauthorized pings (HR/Accounts -> Server) successfully blocked by router firewall.
• Authorized Access: Developer PC successfully connected to Server Room.
• Result: Zero-trust policies completely fulfilled.

## Slide 6: Exp 7: Bank ATM Network
Aim: Simulate a highly available, multi-city ATM WAN.
Requirements:
• Connect critical ATM servers in Patna, Delhi, and Mumbai.
• Extreme fault tolerance and high availability.
• Automatic rerouting during catastrophic physical link failures.

## Slide 7: Exp 7: High Availability Design
• Topology: Redundant 3-city triangular WAN core.
• Protocol: OSPF (Open Shortest Path First) Link-State Routing.
• Mechanism: Dijkstra's SPF Algorithm calculates absolute shortest paths.
• Backbone Area 0: Facilitates rapid sharing of Link State Advertisements (LSAs).

## Slide 8: Exp 7: Failover Simulation
• Convergence Verified: OSPF neighbors established 'FULL' adjacency.
• Failure Simulated: Direct Delhi-Mumbai WAN link intentionally severed.
• Automatic Failover: Tracert utility confirmed immediate rerouting through Patna.
• Result: Zero downtime ATM transaction connectivity maintained.

## Slide 9: Conclusion & Learning Outcomes
• Demonstrated mastery of Layer 2 VLANs and Layer 3 Routing.
• Proven application of NAT and Extended ACLs for cybersecurity.
• Advanced understanding of Enterprise WAN design.
• Real-time implementation of OSPF fault-tolerance in mission-critical systems.